SP-DSA2300/ SP-DSD2300

DSP amplifier

Features:

▪ DANTE network audio optional

▪ Network TCP/IP control, which can manage multiple devices

▪ Constant voltage and constant resistance support: 100V, 70V, 8 ohms, 4 ohms

▪ Remote switch, Power On/Standby setting

▪ Adopt color LCD display

▪ Built-in DSP digital processor

▪ Support multiple connection methods: USB, TCP/IP, RS232, RS485

▪ Real-time remote monitoring of amplifier working status

▪ The amplifier can be identified by software on site

▪ Support balanced XLR input and unbalanced RCA input

▪ Support stereo, bridge, mono, free matrix mode, one-key switch

▪ The input sensitivity can be adjusted in two steps: 0dBu/6dBu, set by software or color LCD screen

▪ Software control, can control media matrix, professional processor at the same time

▪ Wide voltage operation 90-260VAC

Specifications:

Input volume: mute, phase, level detection

Input EQ: 5-band parametric EQ

Input noise gate: start control time 1~2895ms, release time 1~2895ms, start control level -120dBu~-60dBu

DSP matrix: 2*2 matrix

Output EQ: 9-band parametric equalization

Crossover: Butterworth, Bessel, Linkwitz slope 6~48

Output delay: 2*16ms

Output compressor: soft knee, attack level, attack time, compression ratio, release time

Output limiter: start control level -90dBu~21dBu, release time 1~2895ms

Output volume: mute, phase, level detection

DSP presets: 30 preset positions

Control mode: TCP/IP, USB, RS485, RS232

Network specifications: TCP/IP, 1000base-T/100base-TX, RJ45

Web: www.surpass-audio.com; Email: info@surpass-audio.com     Page 1/1